## Slide 1: IVI Introduction
Autotestcon 2016

## Slide 2: What is IVI?
The primary purpose of the Consortium is to:
  Promote the development and adoption of standard specifications for programming test instrument
  Focus on the needs of the people that use and develop test systems who must take off-the-shelf instrument drivers and build and maintain high-performance test systems
  Build on existing industry standards to deliver specifications that simplify interchanging instruments and provide for better performing and more easily maintainable programs
From IVI Foundation By-laws

## Slide 3: IVI fit with other specs
SCPI
GPIB
VXI
AXIe 1.0
PXI
Physical Connection
LXI
PCI, PCIe &
Compact PCI
Ethernet
VME
GPIB
T&M Specific Protocols/Standards
IO Interfaces &
SW Protocols
VXI-11
HiSLIP
VXI
plug&play
PXI-2 and PXI-6: Software
VISA
C/COM/,NET
message
register
IVI 6.3 PXI plug-in
USB TMC
USB
IVI 3.x (Arch)
C
COM
.NET
IVI 4.x(Classes)
Scope
DCPwr
SpecAn
DMM
FGen
ACPwr
Swtch
PwrMe
RFSigGn
Counter
DownCnv
UpConv
Digitiz
Programming
Interfaces for
C/C++/C#/VB
LabVIEW, etc
Instrument
Capabilities
AXIe 2.0
AXIe 3.1

## Slide 4: IVI fit with other specs
SCPI
GPIB
VXI
AXIe 1.0
PXI
LXI
PCI, PCIe &
Compact PCI
Ethernet
VME
GPIB
VXI-11
HiSLIP
VXI
plug&play
PXI-2 and PXI-6: Software
VISA C/COM/.NET
message
register
IVI 6.3 PXI plug-in
USB TMC
USB
IVI 3.x (Arch)
C
COM
.NET
IVI 4.x(Classes)
Scope
DCPwr
SpecAn
DMM
FGen
ACPwr
Swtch
PwrMe
RFSigGn
Counter
DownCnv
UpConv
Digitiz
AXIe 2.0
AXIe 3.1
IO Interfaces &
SW Protocols
Programming
Interfaces for
C/C++/C#/VB
LabVIEW, etc
Instrument
Capabilities
Physical Connection
T&M Specific Protocols/Standards

## Slide 5: IVI Fit with Other Specs
SCPI provided necessary standards based on GPIB needs
  Command strings natural match to GPIB
  HiSLIP allows connection to LXI
VXIplug&play added drivers necessary for VXI
  - Used with other I/O to provide necessary driver
IVI enhances VXIplug&play with new features & support for current tools
GPIB
SCPI
IVI
VXI
VXIplug&play
LXI
PXI
AXIe
HiSLIP
Instrument
Interface
required
required

## Slide 6: Comparing Drivers and SCPI
Programming with SCPI
viPrintf(vi, “MEAS:VOLT? %f, %f”, range, resolution); viScanf(vi, &reading);
  Program deals with strings sent to/from the instrument
  Syntax errors caught by instrument when program is run
  Checking for errors requires another sequence to read error
  Simple model that requires no driver install
Programming with IVI (IVI-C here)
Ag34410_MeasureDCVolt(vi, range, resolution, &reading);
  Program variables sent directly – no chance for SCPI syntax errors
  Syntax errors caught by compiler or editor
  No performance impact due to string manipulation
  Uses debug tools and techniques the programmers knows

## Slide 7: What are IVI Drivers – Really??
Architecture specifications
Instrument class specifications
A library of shared software components
Architecture Specifications
3.1,3.2,3.3,3.4,3.5,3.6,3.9,.3.10,3.12,3.17,3.18
4.1 Scope
4.4 DCPwr
4.8 SpecAn
4.2 DMM
4.3 FGen
4.5 ACPwr
4.6 Swtch
4.7 PwrMeter
4.10RFSigGen
4.12 Counter
4.13DownCnv
4.14 UpConv
4.15Digitizer
~1140 pages of specs
13 specs @ ~220 pages
Notes: Specs
- 3.1 Arch 119 pages
- 3.2 Inherent Cap 178
- 3.3 Cross Class 41
- 3.4 Style 67
- 3.5 ConfigServer 172
- 3.6 Factory 10
- 3.9 C Shared Components 34
- 3.10 MSS 31
- 3.12 FloatingPoint 7
- 3.17 Installation 87
- 3.18 .NET Utility 203
- 4.1 Scope 242
- 4.2 DMM 175
- 4.3 FGen/Arb 202
- 4.4 DC Pwr 76
- 4.5 AC Pwr 176
- 4.6 Swtch 131
- 4.7 PowerMeter 147
- 4.8 SpecAn 106
- 4.10 SigGen 391
- 4.12 Counter 191
- 4.13 DownConvert 179
- 4.14 UpConvert 318
- 4.15 Digitizer 448

## Slide 8: The IVI Architectures
IVI Provides: C, COM, and .NET
C dll for environments that use DLLs
COM Components for COM and .NET ADEs
.NET Assemblies for .NET ADEs
Architectures make use of same class definition
Architectures have specific rules for installation, style, etc.
Details in next section

## Slide 9: IVI Shared Components
IVI Provides several common components to enable multi-vendor systems (more information in the final section)
C Shared Components
Floating Point Services
IVI-COM Session Factory
Configuration Server
COM Type Libraries
.NET PIAs
.NET Shared Components

## Slide 10: What is IVI Compliant -Really??
Common behavior model
Support for IVI Features
  Simulation, IO, doc, ….
Standard install
Common API for common tasks
  ~40 common functions
  Simulation, Caching, Open, Close, Initialize, SW Trigger, Status check, Version ….
Consistent API
  Common organization, data types, naming
Instrument Class API
Custom API still available
  Especially for capabilities beyond the class
Simplifies exchanging instruments
IVI Compliant
Class Compliant

## Slide 11: Why IVI? – Simpler to use
Instantiation, initialization, shutdown
Controlling driver features – state caching, error query, simulation, etc.
Configuration and installation
  Fixed locations for binaries, source, headers, documentation, examples
  Proper registry entries always made
  Common protocol to open/close (standard I/O address is a big benefit)
  Consistent solution for managing driver versions
Standard mechanism for handling multi-channel devices
  aka repeated capabilities in IVI parlance
Standard error reporting
Uniform way of doing common tasks

## Slide 12: Why IVI? – Common Features
Syntactic Interchangeability
Simulation
Fine grained control through properties
Usable in many ADEs
Documentation of SCPI commands used by function
DirectIO (drivers provide access to SCPI)
Attributes for all parameters (fine grained control)
Buildable source for message based instruments (SCPI)
Tested using a IVI-defined process
Key Capabilities that simplify program development
IVI-2014

## Slide 13: Why IVI? – One Driver for any ADE
IVI Drivers (C/COM/.NET) provide a first class experience in nearly any ADE
  Visual Basic 6
  Visual C++
  Visual C# and Visual Basic.NET
  VBA (Excel, Word, PowerPoint)
  LabVIEW
  LabWindows/CVI
  MATLAB
  Agilent VEE
C#, VB
C/C++
VB6

## Slide 14: IVI Registration Page
IVI maintains a registration database
IVI requires that drivers claiming compliance be registered
For users:
  List of drivers, supported instruments
  Mechanism to address defects

## Slide 15: Motivations for IVI.NET
Present an API optimized for .NET
Simplify driver source code
  Allow end users to understand instrument behavior by examining driver source
  Allow end users to modify and add features to drivers on their own
Richer, more expressive APIs
  More flexibility with API data types
  Clean handling of asynchronous notifications (aka “events”)
  Simplified error Handling
Side-by-side deployment of drivers
  Only one version of an IVI-COM or IVI-C driver can be installed at a time
  IVI.NET allows multiple versions of a driver to be installed

## Slide 16: Richer Type System
Both IVI-COM and IVI-C drivers use a limited set of data types
  Integers, floats, Booleans, strings
  Arrays of the above, but extra parameters are required in IVI-C
IVI-C cannot expose an array of strings
IVI-C cannot expose structs
  Can be done in IVI-COM, but it’s tedious to implement
IviScope_FetchWaveform(ViSession vi,
ViConstString channel,
ViInt32 waveformSize, // # of elements on input
ViReal64 waveform[], // actual data buffer
ViInt32 *actualPoints, // # of elements on output
ViReal64 *initialX,
ViReal64 *xIncrement);

## Slide 17: Simplifying APIs with .NET TYpes
IviDigitizer_FetchWaveformReal64(ViSession Vi,
ViConstString ChannelName,
ViInt64 WaveformArraySize,
ViReal64 WaveformArray[],
ViInt64* ActualPoints,
ViInt64* FirstValidPoint,
ViReal64* InitialXOffset,
ViReal64* InitialXTimeSeconds,
ViReal64* InitialXTimeFraction,
ViReal64* XIncrement);
IVI-C signature
Channels[].Measurement.FetchWaveform(IWaveform<Double> waveform)
IVI.NET signature

## Slide 18: Standard IVI.NET Data Types
IVI Foundation felt it would be useful to offer commonly used data types as part of the IVI.NET Shared Components
  Increase consistency amongst IVI.NET drivers
  Facilitate data interchange between drivers
Standardized IWaveform and ISpectrum interfaces
  Digitizers and scopes and RF spectrum analyzers all read waveforms
  Function generators and RF signal generators source waveforms
  Without a common definition of a “waveform”, client applications would need to write the tedious code to translate between each class’s notion of a waveform
Time-based parameters can use PrecisionDateTime and PrecisionTimeSpan
  No confusion about ms vs sec, absolute vs relative time, UTC time, etc
  Precision adequate for IEEE 1588 devices
Common trigger source data type
  Useful in “stitching” together devices in triggered source-measure operations

## Slide 19: How to deal with Events?
IVI-COM and IVI-C drivers almost never expose events
  Exposing something as commonly needed as an SRQ is tortuous
  Requires special knowledge/programming by the driver developer
  Requires special knowledge/programming by the client programmer
.NET supplies a standard mechanism for exposing events
  No special programming required by the driver developer or client programmer
  Trivial code to subscribe/unsubscribe
  Trivial code for driver developers to customize subscribe/unsubscribe semantics
Warnings can now be dealt with properly in IVI drivers by the use of events

## Slide 20: Error Handling in IVI.NET
IVI-C drivers rely solely on return codes
  Errors can easily be ignored by the client application
  After getting the error code, a second function call is required to get the message
  Special handling of warning codes required
IVI-COM error code handling depends upon the client environment
  Return codes in raw C++
  Special exception classes in C++
  COMException class thrown in .NET environments (based on interop)
IVI.NET drivers always use exceptions
  User can always see the full context of the error
  Error content less dependent upon specific driver implementation
  Natural mechanism

## Slide 21: More Information
For more information
  IVI Website: www.ivifoundation.org
  IVI Web Forum: forums.ivifoundation.org
  IVI Instrument Driver Fundamentals Course, Getting Started guides and videos: http://www.ivifoundation.org/resources/default.aspx
  IVI Specifications: http://www.ivifoundation.org/specifications/default.aspx
  IVI Driver Registry: http://www.ivifoundation.org/registered_drivers/driver_registry.aspx
  Most vendors have documentation and drivers on their website
For questions on IVI, go to the IVI Web Forum, open an account, and get answers from member companies.
    IVI Web Forum: forums.ivifoundation.org

## Slide 22
Simplifying Test System Development with IVI.NET
Kirk Fertitta
Pacific MindWorks
: Kirk Fertitta